## Slide 1
Listening at the Fenceline
Six months of continuous community noise monitoring in Howard County, Maryland
Chandra Prakash Choudhary
MS, Geography and Environmental Engineering · Johns Hopkins University
with Dr. Ana María Rule · Dr. Marsha Wills-Karp · Johns Hopkins Bloomberg School of Public Health
CEEJH Symposium · CHARMED Session II: Pilot Projects in Environmental Health Research Bowie State University · 19 September 2026

## Slide 2
INTRODUCTION · 1 OF 3
A community asked the question first
Residents reported a sound that never stopped.
Not a truck passing. Still there at 3 a.m.
A complaint without a measurement has nowhere to go.
By the time anyone arrives with a meter, the sound has changed.
So four households hosted the instruments themselves.
A meter in the back yard, recording every second, for six months.
2

## Slide 3
INTRODUCTION · 2 OF 3
Noise is a health-relevant exposure
Night noise disturbs sleep even if it doesn't wake you up.
The body still responds. WHO set its 45 dB night guideline on that evidence. (2018)
Long-term night noise is linked to high blood pressure and heart disease.
WHO Europe: at least a million healthy life-years lost each year in Western Europe. (2011)
The exposure is not shared fairly, and it is rarely measured.
Industry and highways are located disproportionately in lower-income and minority neighbourhoods.
Air and water have monitoring networks; community noise has almost none.
3

## Slide 4
INTRODUCTION · 3 OF 3
Why we measure Lₑq, and why we propose the use of L90
Leq – the average
All existing guidelines and regulations are based on Leq.
But Leq is an energy average: one dog, one siren, one passing truck can carry a whole night.
L90: the background floor
The level the sound stays above 90% of the time.
Passing events cannot move it. It shows what is always there, which is what a source that never switches off changes.
A normal neighbourhood's background floor drops sharply after dark. A home by a source that operates all night has no such drop. That day-night drop is the measurement.
Decibels are logarithmic: 60 dB + 60 dB = 63 dB. +3 dB is twice the sound energy; +10 dB sounds about twice as loud. All values A-weighted.
4

## Slide 5
METHODS · 1 OF 2
Where we measured
Three homes at the fenceline · one reference home about 2 miles away · all four a similar distance from Rt 32 · Noise measurements collected from 1 March – 31 August 2026, continuous
The reference home is what makes the other numbers mean anything: without it, “48 dB at night” cannot be judged high or ordinary for this region.
5

## Slide 6
METHODS · 2 OF 2
How we measured
Instrument NSRT_W_mk4 logger, factory-calibrated. Meets IEC 61672-1:2002 accuracy; not a certified Class 1/2 meter.
Sampling One A-weighted Lₑq reading per second at each home, about 15 million readings per home over the six months.
Quality control A day or night period counts only if ≥75% of its length was recorded. Exclusions are listed, not dropped.
Placement Rear yard, ~2 m above ground, away from roadways, at the receiving residential property (COMAR 26.02.03.02D; ISO 1996-2).
Criteria WHO 2018: 45 dB at night, health-based. COMAR / Howard County §8.900: 55 dB night, 65 dB day, enforceable.
Analysis Open, version-controlled pipeline; every figure regenerates from the raw files.
6

## Slide 7
RESULTS · 1 OF 2
Average Background Floor Noise by time of day (6 m)
The reference home falls 8.3 dB after dark, to 36 dB in the early hours. Homes C and D fall 1.9 and 3.7 dB and stay near 50 dB around the clock. They have no quiet hours.
7

## Slide 8
RESULTS · 2 OF 2
The background floor, day and night
The reference home goes quiet after dark. The fenceline homes do not.
At night, Homes C and D are louder than the reference neighbourhood is at midday. Their floor stayed above the WHO night guideline on 177 of 177 and 171 of 173 nights.
8

## Slide 9
CONCLUSION 1 of 2
What these measurements do and do not show
What they establish
• Two fenceline homes have no quiet night: their floor stays above the WHO guideline all night, every night.
• Noise is chronic: the pattern held for six consecutive months.
• It is spatially clustered: the two most affected homes are close together and closer to the facility.
• The highway is shared by all four homes; it does not explain the difference.
What they do not
• Source cannot be identified. A meter measures exposure, not origin.
• The reference home crossed 55 dB on more nights than any fenceline home: 28 of 182, against 6, 6 and 18.
• Not a legal measurement loggers that meet IEC 61672-1:2002 accuracy but are not certified Class 1/2.
Control home is a regional reference, not a matched control
We chose the floor as the headline metric because that is what a continuous source affects.
9

## Slide 10
CONCLUSION 2 of 2
Strengths and Limitations
Community-hosted monitoring turned a complaint into a measurement.
An open pipeline and a documented method give a result which a regulator can examine rather than dismiss.
The finding: two fenceline homes have no quiet night.
Continuously elevated for six months, above the WHO night-time health guideline.
The results were reported back to the residents first.
Each household got its own monthly and comprehensive report; one de-identified report lets residents share the findings without revealing location.
Next: a directional Class 1 survey, and monitoring through the seasons.
The only way to confirm a source and test for a tonal character, which would tighten Maryland's night limit to 50 dB.
Limitations:
monitoring was continuous and not screened for wind or rain
data capture varied by month, with March having fewer monitoring days at three homes.
10

## Slide 11
Acknowledgements
Four households let us put an instrument in their back yard for six months. That is the reason this study exists.
Funding by CHARMED Center: National Institute for Environmental Health Sciences (NIEHS) P30 Center for Community Health: Addressing Regional Maryland Environmental Determinants of Disease (CHARMED) Center (grant P30ES032756) Pilot Program; PI: Wills-Karp
The analysis platform is open and online: https://noise-analysis-platform-ga5lsxtezq-uc.a.run.app/
Limitations: monitoring was continuous and not screened for wind or rain ·
COMAR expresses its limits as Lₑq but states no averaging period · data capture varied by month, with March lower at three homes.
References:
WHO Environmental Noise Guidelines (2018) · WHO Europe, Burden of Disease from Environmental Noise (2011) · COMAR 26.02.03 · Howard County Code §8.900 · ISO 1996-1/-2 · IEC 61672-1:2002 · basemap © OpenStreetMap contributors

## Slide 12
Thank You
Questions are welcome

## Slide 13
POCKET SLIDE · FOR QUESTIONS
All measured values, 1 March – 31 August 2026
 | Night L90 (floor) | Day L90 (floor) | Day-to-night drop | Night Lₑq (average) | Day Lₑq (average) | 24-hr Lₑq
Reference home (A), 2 mi away | 39.2 | 47.5 | 8.3 dB | 53.1 | 57.5 | 56.3
Home B, fenceline | 41.5 | 42.9 | 1.4 dB | 48.5 | 54.5 | 53.1
Home C, fenceline | 48.1 | 50.0 | 1.9 dB | 51.7 | 56.9 | 55.6
Home D, fenceline | 48.4 | 52.1 | 3.7 dB | 53.5 | 58.8 | 57.5
These are six-month energy averages over all readings. The night-by-night medians on slide 8 differ slightly. Both are reported.
dB, A-weighted. Night = 10 p.m.–7 a.m. (9 h contiguous); day = 7 a.m.–10 p.m. L90 = the level exceeded 90% of the time; no limit is set on L90. 24-hr Lₑq is all readings combined, not an average of the day and night columns, and not WHO's Lₑₑₙ, which penalises evening and night. WHO night guideline 45 dB; Maryland night limit 55 dB, day 65 dB.
12